## Slide 1
Why is it necessary to cool the cylinder head covers and cylinder liners and pistons of
slow and medium speed engines?
What are the different cooling mediums used for cooling slow and medium speed Engines explain with reasons?

## Slide 2
it is necessary to cool the cylinder head covers and cylinder liners and pistons of
slow and medium speed engines bcz
To keep the material of the engine components in the limit of their thermal and mechanical strengths it is necessary to regulate the heat build up in them. Combustion temperatures exceed metal melting points, causing melting, weakening, and distortion (thermal stresses)
Maintain Lubrication: Prevents lubricating oil oxidation, carbon buildup, and breakdown, which causes piston ring sticking and excessive wear (piston seizure).
Control Thermal Expansion: Minimizes temperature differences to prevent component distortion and maintain tight clearances.
Control Piston Temperature: Essential for piston strength, preventing overheating, and ensuring proper ring function

## Slide 3
Cooling Mediums & Reasons
1. Freshwater (LT - Low Temperature Circuit)
Used For: Cylinder liners and heads (jacket cooling).
Reasons: High specific heat capacity (absorbs lots of heat), good thermal conductivity, non-corrosive (treated), easily circulated through jackets.
2. Lubricating Oil (LO)
Used For: Pistons (especially top/crown)
Reasons: effective for localized cooling of hot piston crowns, good heat transfer Simpler arrangement.
No risk of contamination.
3. Sea Water
Used For: Cooling freshwater circuit (via a cooler) in marine engines, sometimes directly for large engines in air cooler
Reasons: Abundant in marine applications, cheap, removes significant heat; however, it's corrosive and requires a closed freshwater circuit for engine internals.
What are the different cooling mediums used for cooling slow and medium speed Engines explain with reasons?